## Slide 1
Football
Player Tracking System
Image Processing Assignment
N.H.M.S. De Silva
Index: ASP/2023/112
Notes: 1

## Slide 2
Introduction
  Detect and track a single football player in a video
  Convert video into multiple frames (images)
  Segment the player from the background
  Use a tracking algorithm to follow the player
  Implemented using Python and OpenCV
Notes: 2

## Slide 3
Objectives
Frame Extraction
Image Enhancement
Segmentation
Tracking & Analysis
Extract individual frames from a short football clip for per frame analysis.
Improve visual quality (contrast, noise reduction) so detectors perform better.
Separate the target player from background using background subtraction and masks.
Track the selected one player across frames.
Notes: 3

## Slide 4
Tools & Technologies
  Python
  OpenCV (cv2)
  NumPy
  Jupyter Notebook
  GitHub
Notes: 4

## Slide 5
Video & Frame Extraction
  Short video (2–5 seconds) downloaded from YouTube
  Video opened using cv2.VideoCapture()
  Frames read one by one (sequentially)
  Each frame saved as .jpg image
  Frame sampling rate is selected carefully
  Balances quality (details) and processing speed
Notes: 5

## Slide 6
Image Enhancement
  Convert to grayscale to simplify processing.
  Apply Gaussian blur to reduce high-frequency noise.
  Use CLAHE (adaptive histogram equalization) to boost local contrast.
  Apply a sharpening kernel to restore edge clarity for detection.
Enhancement increases signal to noise ratio so segmentation and trackers can perform reliably.
Notes: 6

## Slide 7
Segmentation
  Compares current frame with background model
  Detects moving objects (player)
  Generates a binary mask (black & white image)
  White = player (foreground)
  Black = background
  Uses morphological operations to improve mask
  Erosion removes small noise
  Dilation fills gaps and improves object shape
Notes: 7

## Slide 8
Player Tracking
  Select target using a bounding box on one frame.
  Initialize tracker
  For each subsequent frame, update the tracker and redraw the bounding box.
  Optional: combine mask-based detections to reinitialize tracker if it drifts.
Simple visual feedback: green rectangle shows real-time tracking.
Notes: 8

## Slide 9
Results & Challenges
Results
Challenges
Tracking succeeded in controlled scenes with clear contrast. Image enhancement measurably improved detection rates.
  Fast motion causes motion blur and tracking loss.
  Camera movement (panning/zoom) confuses background subtraction.
  Multiple players in close proximity cause identity swaps.
Notes: 9

## Slide 10
Conclusion & Next Steps
  System can track one football player successfully
  Works well in simple conditions
  Uses basic image processing techniques
  Results are reliable for short videos
  Performance can be improved further
  Enhancements can increase accuracy and robustness
Use AI based detectors (e.g., YOLO) for robust player detection and multi player re identification.
Notes: 10

## Slide 11
Thank You !
This project shows basic image processing can be used for sports analysis.
Notes: 10